## Slide 1: Ultrasound Guidance for Venous Access

## Slide 2: Ultrasound Guidance for Venous Access
Content

## Slide 3: Ultrasound Guidance for Venous Access
Theory - Why ultrasound guidance?
Theory - Basic ultrasound physics
Theory - Anatomy as it relates to ultrasound
Theory - Vascular Access using ultrasound
Agenda

## Slide 4: Ultrasound Guidance for Venous Access
Develop and understand the principles of sound.
Equip you with a basic understanding of the principles of ultrasound.
Develop an understanding of how ultrasound waves are impacted by tissue.
Develop understanding of skills required to perform ultrasound guided vascular access
Learning Outcomes

## Slide 5: Ultrasound Guidance for Venous Access
Hundreds of thousands of vascular access devices placements per year in NHS
  Short - term
  Long - term
Blind landmark technique to locate vessel and guide needle into target vessel increases risks to patient.
Recently ultrasound has been used to access veins for peripheral access (cannula, PICCs, arterial).
Why Ultrasound Guidance?

## Slide 6: Ultrasound Guidance for Venous Access
Ultrasound is the most commonly used imaging technology used worldwide.
Why?
Popular due to:
  Availability – portability
  Speed
  Low cost
  Patient friendly / safety – no radiation
Why Ultrasound?

## Slide 7: Ultrasound Guidance for Venous Access
National Institute for Clinical Excellence (NICE) (2002)
Centre for Disease Control (CDC) (2012)
EPIC3 (2014)
Cochrane Report (Brass et al 2015)
Association for Professionals in Infection Control and Epidemiology (APIC) (2016)
Infusion Nurses Society (INS) (2016)
Association of Anaesthetists of Great Britain and NI (AAGBI) (2016)
Guidelines to support

## Slide 8: Ultrasound Guidance for Venous Access
Randolph (1996)
Rotschild (2001)
Keenan (2002)
Calvert (2003)
Brealey et al (2009)
Lamperti et al(2012)
Cochrane Report – CVC’s (2015)
etc. etc. etc….
Literature to Support

## Slide 9: Ultrasound Guidance for Venous Access
“the use of real-time two-dimensional ultrasound for the placement of central venous catheters substantially decreased mechanical complications and reduced the number of attempts at required cannulation and failed attempts at cannulation compared with the standard landmark placement.”
Literature Support

## Slide 10: Ultrasound Guidance for Venous Access
Missed Target
Multiple Punctures
Failure
Wrong Target
Arterial Puncture
Nerve damage
Blind Technique associated with:

## Slide 11: Ultrasound Guidance for Venous Access
Is not difficult, requires minimal training
Reasonably short learning curve
An excellent teaching tool
Venous Access Using Ultrasound

## Slide 12: Ultrasound Guidance for Venous Access
Definition of US
Mechanical Pressure Wave
Measured in Hertz (HZ)
Basic Ultrasound and Venous Anatomy

## Slide 13: Ultrasound Guidance for Venous Access
Frequency is a measure of pressure cycles over time.
Wavelength is the distance from crest to crest.
Amplitude is the distance of the highest peak or crest value
Wave defined by: Frequency, Wavelength & Aptitude

## Slide 14: Ultrasound Guidance for Venous Access
Inverse relationship between wavelength and frequency
Shorter wavelength = Higher frequency
Longer wavelength = Longer frequency
Wavelength & Frequency

## Slide 15: Ultrasound Guidance for Venous Access
The thickness of the crystal determines the frequency
High Frequency
5 – 10 Mhz
Vibrates at a higher cycle
Wavelength closer together
Less penetration
Shallow structures
Greater resolution
Frequency v Resolution
Low frequency
2 - 3.5 Mhz
Vibrates at a lower cycle
Wavelength spread out
More penetration
Deeper structures
Less resolution

## Slide 16: Ultrasound Guidance for Venous Access
  1. Transducer elements (crystals) convert electrical to mechanical energy and vice versa (Piezoelectric Effect).
2. Initiate sound wave by system
3. Transmission through tissue
4. Causes tissues to compress
5. Reflection off of structures
6. Signal returns to system (transducer)
7. Image produced
This all happens simultaneously
Ultrasound Imaging

## Slide 17: Ultrasound Guidance for Venous Access
Electrical signal produces a series of ‘dots’ on the screen
Need to be aware of anatomy to interpret these ‘dots’
Brightness of dots is proportional to the density of the structure/ time of return
Brighter = More dense (echo return is faster).
Image Formation

## Slide 18: Ultrasound Guidance for Venous Access
US Appearance of Blood Vessels
Brachial vein | Echopoor (BLACK)
Brachial artery | Echopoor
Brachio cephalic Vein | Echopoor (Valves)
Muscles | Less echogenic
Clavicle | Echogenic
Basilic vein | Echopoor
Nerves | Honeycomb appearance

## Slide 19: Ultrasound Guidance for Venous Access
Hypoechoic
Less echogenic than surrounding tissue
Echogenicity
Anechoic
Absence of Echoes
Isoechoic
Same echogenicity as surrounding tissue
Hyperechoic
More echogenic than surrounding tissue

## Slide 20: Ultrasound Guidance for Venous Access
Beam Profile
  Length of the transducer face x 1 mm thick
  Length of beam dependent upon selected depth
Transducer
Beam width – 1mm

## Slide 21: Ultrasound Guidance for Venous Access
Markings are located on one side of transducer only and correspond to orientation marker on screen.
Transducer Orientation

## Slide 22: Ultrasound Guidance for Venous Access
Transverse
Transducer Orientation
Longitudinal

## Slide 23: Ultrasound Guidance for Venous Access
Transducer
Transducer contacts skin
Deeper or away from the skin

## Slide 24: Ultrasound Guidance for Venous Access
Coupling Agent
Ultrasound is reflected at an air interface
Gel provides medium for sound wave into the body by removing air gap
Why use Ultrasound Gel?

## Slide 25: Ultrasound Guidance for Venous Access
Gain controls the brightness of the displayed image
Can be adjusted as near, far or overall
One of the commonest mistakes in ultrasound imaging is the use of incorrect gain settings.
Insufficient gain can result in missed structures of low reflectivity, such as thrombus.
Excessive gain can result in false echos or oversaturation, which may obscure important diagnostic image characteristics such as shadowing or enhancement
Gain

## Slide 26: Ultrasound Guidance for Venous Access
Image Optimization-Gain

## Slide 27: Ultrasound Guidance for Venous Access
The choice of correct depth setting is a trade-off between achieving adequate field of view to resolve all relevant structures and maximising detail resolution.
Depth
Too Close
Too Far
Just Right

## Slide 28: Ultrasound Guidance for Venous Access
You need an understanding of ultrasound physics to help with:
  Transducer selection
  Gain, Depth and Frequency Settings
  Ultrasound modes
  Describing tissue Echo Characteristics
Conclusion

## Slide 29: Ultrasound Guidance for Venous Access
Ultrasound Anatomy

## Slide 30: Ultrasound Guidance for Venous Access
Identify major vascular structures related to vascular access device type
Identify the preferred access vessel for access location
Objectives

## Slide 31: Ultrasound Guidance for Venous Access
Basilic vein:
Preferred vein as it provides the most direct route. Blood flow is greater than the cephalic.
Cephalic vein:
secondary choice as the route is more tortuous.
Veins of the ACF should be avoided as patient movement is restricted and catheter damage may occur.
Brachial Vein: Ultrasound guidance
Applied Anatomy and Physiology

## Slide 32: Ultrasound Guidance for Venous Access
The basilic vein is the first choice for insertion
Originates on the ulnar or medial side of the forearm and ascends on the posterior surface of the arm.
Just before reaching the elbow, it travels to the front of the arm where it joins the median cubital vein.
The basilic vein joins the brachial vein becoming the axillary vein near the armpit.
Basilic Vein

## Slide 33: Ultrasound Guidance for Venous Access
How do we identify these on Ultrasound?
So...

## Slide 34: Ultrasound Guidance for Venous Access
Characteristics of Arteries & Veins
 | Vein | Artery
Appearance | Black | Black
Movement | None ??? | Pulsating
Compressibility | Yes | No
Valves | Yes | No
Size | Usually larger than artery | Usually smaller / rounder

## Slide 35: Ultrasound Guidance for Venous Access
White appearance
Usually non compressible
? CPD
Thrombosis

## Slide 36: Ultrasound Guidance for Venous Access
Ready to go!

## Slide 37: Ultrasound Guidance for Venous Access

## Slide 38: Ultrasound Guidance for Venous Access
Transducers
Linear
Small footprint
5-10 MHz
Transducers

## Slide 39: Ultrasound Guidance for Venous Access
2D greyscale image
Depth/ Focal zone/Gain
Spectral Doppler
 Colour Doppler
Getting the best image

## Slide 40: Ultrasound Guidance for Venous Access
Prepare patient and scanner
Use surgical ANTT:
Full barrier precautions: Gown, sterile gloves, Cap, Mask
Sterile probe cover / Sterile gel
Patient fully draped with fenestration at insertion site
Chlorhexidine 2% in 70% alcohol in single use applicator
Venous Access Using US

## Slide 41: Ultrasound Guidance for Venous Access
Preparing the Probe
Ensure air free coupling between all surfaces

## Slide 42: Ultrasound Guidance for Venous Access
Tilt & Slide the probe to seek out the needle tip.
If you can’t see the tip stop
Work slowly!
Seek out the needle tip

## Slide 43: Ultrasound Guidance for Venous Access
Take control of the probe
Stabilise your hand
Have a cup of tea!
Hold probe correctly

## Slide 44: Ultrasound Guidance for Venous Access
Puncture at steep angle
60o-65o
Relative to the skin
Vessel puncture must
take place in the US beam!
Ultrasound
Probe
Ultrasound Beam
1mm wide

## Slide 45: Ultrasound Guidance for Venous Access
Scan and get target vein in the centre of the screen (ensure that it is compressible)
Place needle in the centre of the probe
Insert needle slowly
Observe vessel wall and look for needle tip prior to puncture
Vessel wall will compress as needle approaches
Stop when needle tip enters vein
Vessel puncture

## Slide 46: Ultrasound Guidance for Venous Access
Watching hands instead of screen
Holding ultrasound probe incorrectly
Collapsing vein with probe pressure
Puncturing at wrong angle
Common mistakes

## Slide 47: Ultrasound Guidance for Venous Access
Routine use of U/S
Familiarise yourself with U/S use and identification of anatomy only
Familiarise yourself with controls
Continue use of phantoms until confident
? Venous access service / radiologists for supervision / support
Next Steps

## Slide 48: Ultrasound Guidance for Venous Access
This patient endured about 30 attempts at ultrasound-guided PICC placement before he said ‘NO MORE!.’
Photo shows about 20 attempts on right upper arm; about 10 more were on the left.
Sent by ambulance (90 miles each way) to a VAS.
PICC placed on first attempt by a vascular access nurse.
It’s not all rosy 

## Slide 49: Ultrasound Guidance for Venous Access
Practice!!